LEAST  SQUARES  UNIT  CELL  REFINEMENT

                                with  INDEXING

                          on the  PERSONAL  COMPUTER







                        Implementation by  Roy G Garvey
                            Department of Chemistry
                         North Dakota State University
                            Fargo,  ND  58105-5516

                                August    1985
                     revised    October   1990

                A  computer  program implementing the procedure of
           Appleman  and Evans (1973) is now available for the
           IBM-PC.   Output of refinement data has been condensed
           for economy of presentation.  For a discussion of
           methodology, see the USGS-GD-73-003 report number 20 by
           Appleman and Evans (1973).


                                     MicroComputers in X-ray Diffraction
                                         Workshop SnowMass, Colorado
                                               6 August, 1985


                      INSTRUCTIONS  for  using  LSUCRIPC


    Demonstration:

         Try some of the examples provided on the diskette before
    proceeding.  With the program diskette in drive  A:, enter LSUCRI,
    specify the filename of the example when asked (e.g. CUBIC.UCR, ORTHO.UCR).

    Creation of Data Files:

         Copy the filenamed TEMPLATE.UCR from the LSUCRIPC System Diskette
    (in Drive A:) to your filename on the diskette in drive B: or to the
    appropriate working sub-directory c:\yoursub\filename.ext.
                     ( For example, COPY A:TEMPLATE.UCR   B:AL203 )

         Bring this new file into your favorite text editor using
    NON DOCUMENT mode.  Replace line 1 with your title.

         Put your cell parameters on line 2.   (Remember to leave at least
    one space between each entry.)  Only the unique cell parameters are
    necessary (e.g. a and c in tetragonal).

         If your crystal system is not orthorhombic, enter your crystal
    system as one of the five-character codes ( CUBIC,  TETRA,  HEXAG,
    HEXAR,  MONOC,  TRICL ) in place of ORTHO.

         Change 60 on line 3 to the largest angle to which you need to have
    2-thetas calculated.

         Look up your absences in the full documentation ( e.g. for P2 1 /c:
    2 in 14 and 2 in 22 ) and carefully count and replace the 0's after
    1.54178  with the appropriate  2,  3  or 4.   Check this entry by counting
    over the systematic absence conditions again.

         In lines 4 and following, in place of the 0's, put in your data
    for h k l (skip two 0's) and 2-theta (ignore the last 0).   When you
    switch from reading alpha to reading alpha-1,  enter the alpha-1
    wavelength (1.5406) in place of the second of the two 0's you skipped.
    This needs to be done only the first time.

         The remainder of the parameters have been left at the default
    values built into the program or set on the TEMPLATE.UCR.  After some
    experience, you may want to modify some of these (e.g.  the tolerances
    and number of refinement cycles).   Note that the program will calculate
    two-thetas for copper K-alpha.  Change the wavelength on line 3 or on the
    first reflection card if you want another radiation.

         Save your file and exit from the text editor.

         Return the LSUCRIPC System Program Diskette to drive A:, or more
    likely, type the name of the .BAT file pointing to the subdirectory
    holding the LSUCRI.EXE file.  For example, the .BAT file might contain
    the lines:

             echo off
             echo  Implementation of Least Squares Unit Cell Refinement
             d:\path\LSUCRI %1 %2

    Enter the name of the batch file, identify your Data File Name when
    prompted, and decide whether you wish to see intermediate data for
    the refinement cycles.  Now sit back to watch the computer work.

         If you get error messages immediately, recheck your data file.
    Look especially for no spaces left between entries or for 0's you may
    have deleted on the systematic absences row. See below for an example of
    the correct format of a data file.



    $ $ $ $      $ $ $ $      $ $ $ $      $ $ $ $      $ $ $ $      $ $ $ $


              D A T A      I N P U T       Definitions and Specifications

         Parameters are  input  with  spaces separating numeric fields:

    FIRST LINE
         Title describing the data being processed.

    SECOND LINE
         Unit Cell Parameters as     A  B  C   Alpha  Beta   Gamma
         Control Parameters  Itht    = 0 for defraction data in 2-theta
                                     = 1 for defraction data in 1-theta

                             thtmx   Maximum  diffraction angle (in Itht
                                      units) to be considered in indexing.
                                      Set at 20 if 0 is coded. 

                             Ncyc   Number cycles during which non-indexed
                                    diffraction with angles exceeding ThtMx
                                    are not accepted in least squares.
                                    A zero value is reset to 2 by program.

                             TolMn  Minimum tolerance allowed (in units of
                                     Itht).  If 0 entered, value reset to
                                     0.02 by program.

                             TolMx  Maximum tolerance allowed (in units of
                                     Itht).  If no greater than TolMn, reset
                                     to five times TolMn.  If given as 0, a
                                     value of 0.1o set by program. 

    THIRD LINE Code for Crystallographic System
                   CUBIC  for cubic crystal systems.
                   TETRA  for tetragonal systems.
                   ORTHO  for orthorhombic systems.
                   MONOC  for monoclinic systems.
                   RHOMB  for rhombohedral or trigonal systems.
                   TRICL  for triclinic systems.
                   HEXAG  for hexagonal systems.
                   HEXAR  for hexagonal-rhombohedral systems.

         TheMx    Value comensurate with Itht to be used in determining the
                   minimum interplanar spacing for generated diffraction. 
                   This value may be superceded by given diffraction having 
                   greater Bragg angles.  If 0 and there are no observed 
                   diffraction given, TheMx is set to 90o theta.

         Pwl     Primary wave length used in computing minimum distance for
                   generater diffraction.  If given as 0,  value of 1.5405 A
                   is assumed.

          The next 27 entries indicate conditions for non-extinction for
    certain diffraction classes.   To be effective, the integer n entered
    must be 2,3 4 or  6 in the appropriate location;  x,  y,  and z are any
    integers.   If the crystal type is HEXAR,  entry 6 will be considered
    to be 3 whether it is entered or not by the user.  Each of the following
    27 items must be represented by a numeric value as described above or by
    0 as a place holder.  Each entry must be separated form those preceding
    and following by at least one space.

                                Class of           Condition for
                 Entry        Diffraction          non-extinction
                   1              hkl                h + k = x.n
                   2              hkl                h + l = x.n
                   3              hkl                k + l = x.n
                   4              hkl       h+k = x.n, h+l = x.n, k+l = x.n
                   5              hkl            h + k + l = x.n
                   6              hkl           -h + k + l = x.n
                   7              hhl                    h = x.n
                   8              hhl                    l = x.n
                   9              hhl                h + l = x.n
                  10              hhl               2h + l = x.n
                  11              0kl                    k = x.n
                  12              0kl                    l = x.n
                  13              0kl                k + l = x.n
                  14              h0l                    h = x.n
                  15              h0l                    l = x.n
                  16              h0l                h + l = x.n
                  17              hk0                    h = x.n
                  18              hk0                    k = x.n
                  19              hk0                h + k = x.n
                  20              hh0                    h = x.n
                  21              h00                    h = x.n
                  22              0k0                    k = x.n
                  23              00l                    l = x.n
                  24              hll                    h = x.n
                  25              hll                    l = x.n
                  26              hll                h + l = x.n
                  27              hll               h + 2l = x.n

              SEmult   Multiple of the standard error of an observation of
                        unit weight to be used in setting tolerances.

    FOURTH and following LINES
         Diffraction data.  For diffraction that are to be indexed by the
    program by comparing corresponding distances and angles with those of
    theoretical diffraction, h, k, and l must be given as zero.  If one or
    more of the diffraction indices is non-zero, the indices read from the
    diffraction entry will be maintained throughout the run.  Diffraction
    entries must be arranged in order of increasing Bragg angle (or decreasing
    d-spacing).  If no observed diffraction data are given, the output will
    consist of theoretical lines only.  As before, numeric entries are
    separated by spaces.   0 is entered as a place holder where no data is
    input.   Each diffraction is represented by the following entries:

              h  k  l   D    Wlc   Obs     Wt

    where h,  k,  l are the corresponding Miller indices.   D is the
    interplanar spacing as computed from the Bragg relationship.  D need not
    be given if OBS is  given.   Wlc  is the wavelength (in A) associated
    with the current diffraction.   If given as 0, it is assumed to be the
    same as the wavelength for the previous diffraction line.  (If a
    wavelength for the first diffraction line of a data set is not given,
    the value given or implied by Pwl is used).  Obs is the Bragg angle
    concomitant with Itht and given as degrees and fraction thereof.   The
    angle need not be given if D is given.  If both theta and D are given,
    D will be recomputed as the observed d-spacing from theta and the given
    or implied wavelength.  WT is the weight to be associated with the
    value of theta for the current diffraction.  If WT is given as 0,  it is
    set to 1.0 by the program.   All entries are set to 0 for the last data
    line.

         A sample data set is included illustrating the use of 0 as place holder.

    Cell Refinement of A - ZrPO4    SNOWMASS  WORKSHOP   test data file.
    9.06  5.295 15.414 90 101.75 90 0 0 0 0 0
    MONOC  73  0.0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0.0
     0  0  2 0.0 1.5405981 11.7087 0.0
    -1  1  1  0   0        19.8162  0
     2  0  0  0   0        20.0178  0
     0  1  2  0   0        20.4939  0
     2  0  1  0   0        22.072   0
    -1  1  3  0   0        24.9746  0
     2  0  2  0   0        25.2411  0
    -2  1  2  0   0        27.0218  0
     1  1  3  0   0        27.7465  0
     0  1  4  0   0        29.0032  0
    -3  0  1  0   0        29.5801  0
    -1  1  5  0   0        33.8194  0
     0  2  0  0   0        33.8903  0
    -3  1  1  0   0        34.1718  0
    -3  1  2  0   0        34.655   0
     0  2  2  0   0        35.9646  0
    -3  1  3  0   0        36.1483  0
     3  1  1  0   0        36.301   0
    -2  0  6  0   0        37.2433  0
     1  1  5  0   0        37.3402  0
     0  2  3  0   0        38.4033  0
    -3  1  4  0   0        38.572   0
     3  1  2  0   0        38.7756  0
    -2  2  2  0   0        40.2341  0
     4  0  0  0   0        40.6483  0
    -2  1  6  0   0        41.0746  0
     0  2  4  0   0        41.6506  0
     3  1  3  0   0        42.0089  0
     2  2  2  0   0        42.6968  0
    -4  0  4  0   0        42.8435  0
    -4  1  1  0   0        43.5333  0
    -1  1  7  0   0        44.4877  0
     4  0  2  0   0        44.8181  0
    -2  0  8  0   0        48.2941  0
     1  1  7  0   0        48.4369  0
    -1  3  1  0   0        53.0391  0
    -4  2  2  0   0        53.3706  0
    -5  1  3  0   0        54.0075  0
    -1  2  7  0   0        54.1143  0
    -1  3  3  0   0        55.4481  0
    -4  2  4  0   0        55.7147  0
     1  2  7  0   0        57.5746  0
    -3  2  7  0   0        58.9394  0
     2  1  8  0   0        59.4316  0
    -2  2  8  0   0        60.2872  0
     3  1  7  0   0        60.4909  0
    -5  1  7  0   0        63.1216  0
     1  2  9  0   0        68.7137  0
    -4  1 10  0   0        70.0417  0
     0  4  0  0   0        71.2907  0
    -6  2  2  0   0        71.9717  0
     0  0  0  0   0         0.0     0

         Specific parameters are identified in the following lines of input
    data.  Note that spaces are used as "field Delimiters".

    TITLE LINE
    Cell Refinement of A - ZrPO4    SNOWMASS  WORKSHOP   test data file.

    UNIT CELL PARAMETERS                                    Tolerance
      A     B     C     aLpha   beta   gamma   Itht thtmx  ncyc   mn   mx
    9.06  5.295 15.414   90     101.75  90      0     0     0      0    0
        T
        h
        e        Conditions for non-extinction for certain classes
        m                        1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2
Sysext  x  Pwl 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 Semult

MONOC  73  0.0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0.0

     DIFFRACTION DATA
      h  k  l  D    Wlc      Angle   Weight

      0  0  2 0.0 1.5405981 11.7087   0.0
     -1  1  1  0       0    19.8162    0
      *  *  *  *       *       *       *

     TERMINATOR of H K L DATA INPUT
      0  0  0  0       0       0       0